## Slide 1
Ammonia Advance
8/26/2010 ETO chloramine
<number>

## Slide 2: Water, Water everywhere!
8/26/2010 ETO chloramine
<number>
Water treatment is like a puzzle. On the following slides we will take a close look at Ammonia Measurement (NH3).
H2O
ClO2
NH3
Cl2
Na
Fe
NH4
Ag
Cu

## Slide 3: Markets
Drinking water treatment.
Wastewater treatment.
Irrigation water.
Cooling towers.
Explosive manufacturing.
Plastic manufacturing.
Textile industry.
Aquatic market.
Zoo’s and Aquariums.
8/26/2010 ETO chloramine
<number>

## Slide 4
8/26/2010 ETO chloramine
<number>
NEW Products - Ammonia Analyzer
20 ppm NH3
Potentiometric sensor
Reagentless
Datalogging
Ethernet & ModBUS
Applications
Potable water
Cooling towers/chillers
Nitrification processes
<number>

## Slide 5
8/26/2010 ETO chloramine
<number>
<number>
Back panel
<number>
Note: At ambient temperature Ammonia is lighter than air.

## Slide 6
8/26/2010 ETO chloramine
<number>
<number>
Log on screen
<number>

## Slide 7
8/26/2010 ETO chloramine
<number>
Free ammonia
N
H
H
H
N
107o
H
H
H
..
NH3
..
H
H
H
N
Trigonal
Pyramidal
geometry
N
H
H
H

## Slide 8: Basic chemical properties of Ammonia.
8/26/2010 ETO chloramine
<number>
Ammonia is a colorless gas with a very pungent odor.
It is lighter than air at ambient temperature.
Ammonia dissolves easily in water to form Ammonium Hydroxide.
Ammonia in water is pH dependent.
NH3 = Free ammonia
NH4 = Ammonium

## Slide 9: Examining
8/26/2010 ETO chloramine
<number>
Now let us look at what happens when ammonia is added to water that contains metals and other impurities.

## Slide 10: Reaction between copper and ammonia.
8/26/2010 ETO chloramine
<number>
Cu2+ --> Cu(NH3)42+
Depending on the levels of copper and ammonia in the solution the different range of colors below would form.

## Slide 11: Colors of some other Ammonia compounds.
8/26/2010 ETO chloramine
<number>
NH3 = Ammonia
N03 = Nitrate
CoBr = Cobalt Bromide (Coagulant used in Waste Water)
NO2 = Nitrogen Dioxide

## Slide 12: Ammonia – complexes silver and dissolves AgCl
8/26/2010 ETO chloramine
<number>
Aqueous ammonia
Precipitates brown
Ag2O:
2Ag+(aq) + 2NH3(aq) + 2H2O(I) <==>
Ag2O(s) + 2NH4+(aq) + H2O(I)
Note: The silver (I) oxide
precipitate dissolves in
excess ammonia to form
a colorless complex ion.

## Slide 13
8/26/2010 ETO chloramine
<number>
Temperature effect on ammonia

## Slide 14
8/26/2010 ETO chloramine
<number>
<number>
Ammonia Equilibrium
> Most competitors display what ammonia exist at
ambient temperature.
>Prominent Ammonia analyzer measures the ammonia
under process conditions.
Temperature effect on ammonia equilibrium:
Note: System can be programmed to display the incorrect level at
ambient temperature if you want.

## Slide 15: Competition
Chemscan
  Requires reagents.
  Does not measure under process condition.
  Calculates the free ammonia – does not read it.
Hach APA 6000
  Requires reagents.
  Does not measure under process condition.
  Complicated System, may require a service contract.
ATI
  Requires reagents.
  Calculates the free ammonia – does not read it.
8/26/2010 ETO chloramine
<number>

## Slide 16
8/26/2010 ETO chloramine
<number>
<number>
EPA table NH3 vs. pH & Temperature
Note: Un-ionized form = NH3

## Slide 17
8/26/2010 ETO chloramine
<number>
<number>
Solubility curves
As you look at the table you will see
as temperature is reduced NH3 becomes
more soluble and NH4 is less soluble.

## Slide 18
8/26/2010 ETO chloramine
<number>
<number>
Web ammonia calculator can be used for
independent verification of reading.
http://cobweb.ecn.purdue.edu/~piwc/w3-research/free-ammonia/nh3.html
Perdue has an ammonia calculator available on the web @ the address listed below:
Simulation below is from an actual application our analyzer read 0.02 our competitors
read 0.15.

## Slide 19: pH and NH3
8/26/2010 ETO chloramine
<number>
Remember NH3 concentration
is pH and temperature dependent.

## Slide 20
8/26/2010 ETO chloramine
<number>
Amino Acids – Functional Groups
Amine
Carboxylic Acid
Base Pair
NH21-
R- COOH
NH3
NH21-
NH41+
amine
ammonia
ammonium ion
N
H
H
H
:
N
H
H
H
H
:
1+
N
H
H
:
1-
:
H+
lose H+

## Slide 21
8/26/2010 ETO chloramine
<number>
Chloramination
Chloramination Monitoring

## Slide 22
8/26/2010 ETO chloramine
<number>
What are Chloramines?
Chemicals that are formed when chlorine and ammonia are combined in water.
  Monochloramine (NH2Cl)
  Dichloramine (NHCl2)
  Trichloramine (NCl3)

## Slide 23
8/26/2010 ETO chloramine
<number>
HOCL

## Slide 24
8/26/2010 ETO chloramine
<number>
Monochloramine

## Slide 25
8/26/2010 ETO chloramine
<number>
Dichloramine

## Slide 26
8/26/2010 ETO chloramine
<number>
Trichloramine

## Slide 27
8/26/2010 ETO chloramine
<number>

## Slide 28
8/26/2010 ETO chloramine
<number>
<number>
pH Chloramines
<number>

## Slide 29
8/26/2010 ETO chloramine
<number>
Chloramination Breakpoint Curve

## Slide 30
8/26/2010 ETO chloramine
<number>

## Slide 31
8/26/2010 ETO chloramine
<number>

## Slide 32
8/26/2010 ETO chloramine
<number>
Weights
Example: If 71 pounds of chlorine gas was added to water
containing 17 pounds of free ammonia ratio would be 1:1.

## Slide 33
8/26/2010 ETO chloramine
<number>
Note: On test sites operators were targeting < 0.2 PPM
Of NH3.

## Slide 34
8/26/2010 ETO chloramine
<number>
Remember to leave enough
reaction time before the
taking the sample.

## Slide 35
8/26/2010 ETO chloramine
<number>

## Slide 36
8/26/2010 ETO chloramine
<number>

## Slide 37
8/26/2010 ETO chloramine
<number>
Benefits of Chloramine (compared to chlorine)
More Stable
Less Reactive (reduced THM formation)
Longer Lived Residuals
Effective Secondary Disinfectant
Minimizes Objectionable Taste and Odors

## Slide 38
8/26/2010 ETO chloramine
<number>
Optimal Chloramination Control Range
Note: Watch the ratios and what is being measured NH3 = 4:1 max.,
NH3-N 5:1 max.

## Slide 39
8/26/2010 ETO chloramine
<number>
Chloramination Control Challenges
Maintain Adequate Disinfectant Concentration to Ensure Safe Water
Feed Enough Ammonia to Prevent Di and Trichloramine Formation and Prevent Drop in Chlorine Residual
Prevent Over Feed of Ammonia to Minimize the Potential of Nitrification in the Reservoirs and Distribution System
On-Line Analysis Provides the Information Required to Control the Chloramination Process

## Slide 40
8/26/2010 ETO chloramine
<number>
Breakpoint as Measured by Free and Total Chlorine Analyzers
A Total Chlorine result has 3 possible locations on the breakpoint curve
Free Chlorine reacts with Monochloramine giving a false reading until beyond the Breakpoint
First Indication of Free Chlorine is AFTER Dichloramine Formation

## Slide 41
8/26/2010 ETO chloramine
<number>
Breakpoint with Fixed Cl2

## Slide 42
8/26/2010 ETO chloramine
<number>
Chloramination Control Strategies
Ratiometric control
  Cl2 : NH3-N ratio between 3:1 and 5:1
  Measures total chlorine from all forms and total ammonia from all forms (free and combined)
Residual control
  Maintain small free ammonia residual
  Maintain target monochloramine

## Slide 43
8/26/2010 ETO chloramine
<number>
Chloramines are Effective Disinfectants
Monochloramine has Least Odor and Taste
Chloramination can be Difficult to Control
  Too little ammonia cause di and trichloramine formation and loss of chlorine residual
  Too much ammonia can cause nitrification in reservoirs and distribution system
Effective On-Line Analysis Equipment will Aid in the Control of the Chloramination Process
Summary

## Slide 44
8/26/2010 ETO chloramine
<number>
NEWWA summary slide

## Slide 45: Reference links
8/26/2010 ETO chloramine
<number>
http://nfbwa.com/pdf-docs/2009/SWConversionWorkshopPresentations/DAM5%20Applying%20Chloramines%20(Course%20Manual%20v7).pdf
http://www.newwa.org/PDF/AnnConf08-SessD1010.pdf

## Slide 46
8/26/2010 ETO chloramine
<number>
Any Questions?