## Slide 1: ProMinent Beta/b Pump

## Slide 2: New Beta/b Pump
New
Physical redesign
New external contact
Similar capacity ratings/models to Beta/a
  Models 1005 and 1605 are no longer available
  New models 1604, 2001, 2002, and 2504

## Slide 3: New external contact
External contact input with Pulse Control as standard
  Range 1:64 – 64:1
  Adapted for water meters, etc.
  Optimal efficiency of the pump
  No additional devices required

## Slide 4: Beta/b
New liquid ends with PVDF valves and PTFE seals for all plastic dosing head materials
  PPT, NPT, PVT
  NPE and NPB liquid ends only available on auto-degassing models
  Beta/a liquid ends will fit on Beta/b drives.
  Beta/b liquid ends will fit on Beta/a drives

## Slide 5: Beta/b Capacities
Pump type | Stroke frequency | Capacity | Backpressure
 | (spm) | (gph) | (psi)
BT4b 1000 | 180 | 0.20 | 145
BT4b 1601 | 180 | 0.29 | 232
BT4b 1602 | 180 | 0.58 | 232
BT4b 1604 | 180 | 1.00 | 232
BT4b 0708 | 180 | 1.88 | 102
BT4b 0413 | 180 | 3.25 | 58
BT4b 0220 | 180 | 5.02 | 29
BT5b 2504 | 180 | 0.77 | 363
BT5b 1008 | 180 | 1.80 | 145
BT5b 0713 | 180 | 2.91 | 102
BT5b 0420 | 180 | 4.52 | 58
BT5b 0232 | 180 | 8.45 | 29

## Slide 6: Liquid end materials
Material | Liquid End | Valves | Seals | Valve Balls
PPT | Polypropylene | PVDF | PTFE | Ceramic
NPT | Acrylic | PVDF | PTFE | Ceramic
PVT | PVDF | PVDF | PTFE | Ceramic
TTT | PTFE | PTFE | PTFE | Ceramic
SST | SS | SS | PTFE | Ceramic