## Slide 1: New ClO2-Generators Bello Zon® CDVc
Dr. Matthias Rothe
ProMaqua GmbH
Maaßstraße 32/1, D-69123 Heidelberg
Tel. +49 (6221) 6489-0, Fax. +49 (6221) 6489-400
m.rothe@promaqua.com www.ProMaqua.com
Notes: <number>

## Slide 2: New Features of CDVc
unique plant for production, dosage and measurement of chlorine dioxide
  controller with integrated measurement of chlorine dioxide and/or chlorite
  central administration of up to 14 dosing and measurement points
reactor and reactor outlet made of PVDF
chemical feed pumps with stroke length monitoring
  automatic calculation of the capacity after changing the stroke length
  failure message at accidental changing of the stroke length
simple and safe operation and servicing
  operating menu with plaintext advices and data logger
  integrated calibration assemblies
  reduced number of wear and tear parts

## Slide 3: Bello Zon CDVc for Diluted Chemicals
Dr. Rothe, 08.10.08
PVDF reactor and reactor-outlet
reactor cover as splash guard and blinds
reactor housing w. suction assembly (optional)
torsion mixer
deep drawn panel
dosing pumps in CAN-bus version
controller with data logger and screen recorder
calibration and suction aid with vacuum pump (optional)
single stroke flow sensor

## Slide 4: Capacity Range CDVc
type | ClO2-output [g/h] | operating pressure [bar] | operating temperature [°C]
CDVc 20 | 1-20 | 8 | 10-40
CDVc 45 | 2-45 | 8 | 10-40
CDVc 120 | 6-120 | 8 | 10-40
CDVc 240 | 12-240 | 8 | 10-40
CDVc 600 | 30-600 | 8 | 15-40
CDVc 2000 | 100-2.000 | 5 | 15-40
Dr. Rothe, 08.10.08

## Slide 5: Bello Zon CDKc for Concentrate Chemicals
Dr. Rothe, 08.10.08
Design will follow during 2009

## Slide 6: Prospective Capacity Range CDKc
type | ClO2-output [g/h] | operating pressure [bar] | operating temperature [°C]
CDKc 170 | 170 | 8 | 10-40
CDKc 420 | 420 | 8 | 10-40
CDKc 900 | 900 | 8 | 10-40
CDKc 2100 | 2.100 | 7 | 10-40
CDKc 3000 | 3.000 | 5 | 15-40
CDKc 7500 | 7.500 | 2 | 15-40
Dr. Rothe, 08.10.08

## Slide 7: Basic Concept New Series CDVc and CDKc
controller similar to Dulcomarin II
  direct connection of 2 amperometric sensors: measurement and display of chlorine dioxide and chlorite (mA-sensors, not CAN-Sensors!!)
multiple interfaces (under discussion)
  Profibus DP
  LAN
  WEB-server
  ISDN
  analogue
  GSM
Dr. Rothe, 08.10.08

## Slide 8: Concept Controller New Series CDVc and CDKc
multicolor display of Dulcomarin II
  simple, self-explaining operation
  integrated screen recorder and data archiving
stroke length monitoring of the metering pumps
  automatic calculation of the capacity after changing the stroke length
  failure message at accidental changing of the stroke length
Dr. Rothe, 08.10.08

## Slide 9: Controller New Series CDVc and CDKc
relay output for normal operation status
relay outputs warning and alarm freely configurable
digital remote control input freely configurable for function pause or high dosage
wide range power supply 90-240 V, 50/60 Hz
connection of up to 14 auxiliary modules via CAN-bus
Dr. Rothe, 08.10.08

## Slide 10: Universal Auxiliary Module
use as controller for intermediate storage tanks: BatchControl
use as measurement and control unit: DosControl
Dr. Rothe, 08.10.08

## Slide 11: Universal Auxiliary Module
Legio Zon-housing (D1C-display und -keypad)
change of functionality Batch/DosControl via internal jumper
sheet with labels DosControl, BatchControl, node-ID, blanks
Dr. Rothe, 08.10.08

## Slide 12: Bello Zon BatchControl: Controller Storage Tank
use as separate control unit for intermediate storage tank
  4 inputs for level switches
  pause input
  output for solenoid valve dilution water
  output for solenoid valves ClO2-solution
  output for control of pneumatic valve for air supply of pneumatic pumps
  alarm relay output
  universal communication interface for commercial modules (e.g. for failure message via SMS)
Dr. Rothe, 08.10.08

## Slide 13: Bello Zon DosControl : Measurement
administration of up to 14 modules in the central controller
  measurement / documentation in the central controller
  parameter settings in the central controller
  calibration of probes in the module
measurement parameters:
  chlorine dioxide and chlorite (mA-sensors, not CAN-Sensors!!)
  redox potential (mV) and pH (mV)
  temperature (PT 100 or 1000)
further in-/outputs: pause, measurement water, operation relay, failure relay
universal communication interface for commercial modules (e.g. for failure message via SMS)
Dr. Rothe, 08.10.08

## Slide 14: Bello Zon DosControl : Dosage of ClO2
administration of up to 14 modules in the central controller
PID controller for chlorine dioxide
output ClO2-pump or ClO2-valve
further in-/outputs: pause, measurement water, operation relay, failure relay, basic load
universal communication interface for commercial modules (e.g. for failure message via SMS)
Dr. Rothe, 08.10.08

## Slide 15: Identcode CDVc
type and capacity
power supply:
U 100-230 V, 50/60 Hz for all types without bypass for storage module with water supply 230 V, reactor housing or integrated bypass pump due to the solenoid valves and pump 230 V
A 230 V, 50/60 Hz for all types with integrated bypass pump, reactor housing or bypass for storage module with water supply 230 V
B 100-115 V, 50/60 Hz for all types without integrated bypass pump or bypass for storage module with water supply 230 V (pump and solenoid valve 230 V)

## Slide 16: Identcode CDVc
bypass:
00 without e.g. as base for complete pipework made of PVDF
02 bypass PVC-U with float type flowmeter; DN 25 at CDVc 20-600, DN 40 at CDVc 2000
04 bypass PVC-U DN 25 with float type flowmeter and stainless steel bypass pump 230 V (CDVc 20-600, only)
06 bypass for ClO2-storage tanks with water supply module 230 V and smaller float type flowmeter (CDVc 45-600, only)
07 like 06, but with water supply module 24 V (separate 24 V-supply required)

## Slide 17: Bypass for ClO2-Storage Tanks
water feed assembly for installations with intermediate ClO2-storage
  float type flow meter in the bypass suitable for flow rates required to produce 500 – 1000 ppm ClO2
  230 V-version: solenoid valve to be directly connected to the controller
  24 V-version: interconnected transformer or relay required (accessory; transformer: part number 1035156)
standardized storage tanks will follow during 2009
Product management, Dr. Rothe, 03.06.08
filter
pressure reducer
solenoid valve
water meter
needle valve

## Slide 18: Identcode CDVc
reactor housing with suction device:
0 without, without calibration device
1 without, with calibration device
2 with, without calibration device power supply
3 with, with calibration device A or B, only
suction lances / assemblies:
via identcode available for CDVc 20-600
level switches (round plug, only) have to be connected directly to the pumps!

## Slide 19: Identcode CDVc
control features:
0 base version
1 with measurement of ClO2 and chlorite and PID-controller
2 like 1, but with data logger and screen recorder
in- and outputs:
0 standard: 4 digital inputs for pause or high-dosage, leakage, external fault and sample water, 1 contact or frequency input water meter
1 two analogue inputs 0/4-20 mA, free configurable for for amperometric probes (ClO2 or chlorite), actuating variable or flow
2 analogue output 0/4-20 mA, free configurable
3 combination of features 1 and 2

## Slide 20: Accessories
flushing assembly
  scope of delivery as important safety feature (required for commissioning), no separate order required
vent valve as vacuum breaker in the bypass pipe
  not scope of delivery
  has to be ordered separately via part number 1001260
back pressure valve DHV-RM
  required for bypass without back pressure
  DN 25: part number 1000050 (CDVc 20-600)
  DN 40: part number 1000052 (CDVc 2000)

## Slide 21: Pricing
base version: same pricing such as with CDVb or CDVa, price advantage with several advanced versions
e.g. 45 g-plant with pause and analogue in-/output
  CDVb1A00313D110: € 9.854,00
  CDVc04PU02000DE03… € 9.536,00 (without reactor housing)
  CDVc04PA02200DE03… € 10.056,00 (with reactor housing)
e.g. 45 g-plant with measurement and control features
  CDVb1A00313D110 + D1C: € 10.883,00
  CDVc04PU02000DE13… € 10.211,00 (without reactor housing)
  CDVc04PA02200DE13… € 10.731,00 (with reactor housing)

## Slide 22: Schedule Availability
CDVc without communication interfaces
  20 – 240 g/h: January 2009
  600 g/h: spring 2009
  2000 g/h: summer 2009
CDKc without communication interfaces
  up to 900 g/h: mid 2009, larger plants by end of 2009
auxiliary modules BatchControl and DosControl
  mid of 2009
communication interfaces such as LAN, Profibus etc.
  autumn 2009
Dr. Rothe, 05.11.08

## Slide 23: Thank you for your attention
Any questions?