## Slide 1: NEW Dulcometer Compact Controller

## Slide 2: Compact Controller for pH/ORP
The Compact Controller has a fixed configuration (fixed number of inputs/outputs and a fixed software configuration)
Order under p/n 7781499 (inc. power cord)
List price is $830.00
29.07.26
<number>

## Slide 3: Compact Controller for pH/ORP
Features:
Measured variables
pH and ORP/Redox switchable
Enclosure rating:
Nema 6 (IP 67)
Dimensions:
5.3“ x 4.9“ x 2.95“ (H x W x D)
29.07.26
<number>
Notes: <number>

## Slide 4: Compact Controller for pH/ORP
Features:
Control directions:
One control direction (selectable lowering↓ or raising↑ of a value)
Loop control / functions:
1-way P or PID loop controller
1 pulse frequency output
1 power relay as alarm or limit or solenoid
1 mA output 4…20 mA (measured value or control output)
Priming function (↑↓- press simultaneous) acts on all outputs
29.07.26
<number>
Notes: <number>

## Slide 5: Compact Controller for pH/ORP
Features:
Measuring ranges
pH: 0.00…14.00
ORP/Redox: -1000 … + 1000mV
Temperature compensation for pH via Pt1000
Compensation range: 32 … +248°F
Power supply:
90 – 253V, 50/60 Hz
Temperature range (operation)
Ambient temperature -14 ... +140°F
29.07.26
<number>
Notes: <number>

## Slide 6: Compact Controller for pH/ORP
Additional features
pH sensor check
Checks if sensor is not connected and if sensor input is disrupted.
Checkout time for LIMIT and CONTROL (LIMIT ERR)
Monitoring of the control output (monitoring of the control output level for a checkout time), puts control output to basic load - no automatic reset
Monitoring of the limits for a TIMELIM, stops control if limits are exceeded for longer than TIMELIM, automatic reset
Error Log
The last 3 errors are kept in display
29.07.26
<number>
Notes: <number>

## Slide 7: Compact Controller for pH/ORP
Features:
Password protection:
Free access = 5000
master password are the last 4 digits of the serial number (e.g. Serial number = 2010012458
29.07.26
<number>
Notes: <number>

## Slide 8: Compact Controller pH/ORP - Terminals
29.07.26
<number>

## Slide 9: Display and Operation
29.07.26
<number>

## Slide 10: Operation of Compact Controller – key pad
29.07.26
<number>
Old key
Old key
Old key
New „i►“ key
New Compact Controller key pad

## Slide 11: Operation of Compact Controller
29.07.26
<number>

## Slide 12: Operation of Compact Controller
29.07.26
<number>

## Slide 13: Operation of Compact Controller
29.07.26
<number>

## Slide 14: Compact Controller key pad – CAL-key
29.07.26
<number>

## Slide 15: Compact Controller Menu overview with – i ► - key
29.07.26
<number>

## Slide 16: Compact Controller Menu Outline
29.07.26
<number>