## Slide 1: D1Cb FW Update with USB adapter and Upgrade via Activation Key
Dietmar Berger
Productmanager Business Unit Measuring & Control Technology
16th June 2009
Notes: <number>

## Slide 2: D1Cb FW Update with USB adapter and Upgrade via Activation Key
Upgrade – Update
There is a difference between firmware update and identity code upgrade
Why is a firmware (another name for software) update of a controller necessary?
  To clear software bugs
  To add new functions
  To add new languages.
If a firmware update is necessary you will be informed by ProMinent Heidelberg (email, MMP info)
A firmware update is without any costs.

## Slide 3: D1Cb Upgrade with Activation Key
The upgrade possibility with Activation Key allows you to store D1Cb controllers with basic configuration.
You can immediately deliver a customized controller after the wishes of your customer
All possible identity code configurations are supported by the D1Cb´s hardware without any additional hardware
The price for the upgrade is given in the D1Cb´s price list.
Your normal conditions are valid for the Activation Key upgrade.
There are two ways to put the Activation Key in the D1Cb
  You can do it with the D1Cb´s key pad
  Or with a Windows PC, USB to CAN adapter and PC Update Software

## Slide 4: How to make a firmware update?
Install the software “language and firmware update” on your Windows PC (use the corresponding manual)
Follow exactly the manual!
Do not connect the USB adapter before or during installation. Connect it after installation and after reboot!
During installation, do answer all reboot requests with “NO”
But install .NET and IXXAT driver.
Use for help the manual
Build the programming adapter connection, shown on small manual small manual page A3-14 / 15
After complete installation reboot the PC
Connect the IXXAT USB to CAN adapter
Download the latest firmware and language data files from the service page (technical documents, search after D1Cb software)
Connect the USB to CAN adapter to the D1Cb like shown in the manual

## Slide 5: How to make a firmware update?
Download the firmware and language files from the service page
Search after: D1Cb software
Copy the files to your PC
Start the PC program
Choose what you want to do (Firmwareupdate / Languageupdate update)
Load the downloaded files
Click “start updates”
If the power drops while updating or something else breaks the connection use the “recovery mode”.

## Slide 6: Identity code upgrade
You need the following informations of the D1Cb:
  Equipment number, you can find this number in the menu “General Settings und Informations” or on the type plate of the D1Cb
  The identity code value you want to change
The identity code of the D1Cb in the Activation Key application on the service page is preset to the basic identity code settings – they are for free. The values with costs are marked.
If you want to upgrade an identity code value, you change only this value of the identity code in the Activation Key application you want to expand.
The rest of the values stay on the basic settings
If an already upgraded D1Cb must be expanded a second/third time you change only this relating value of the identity code.
The rest of the values stay again on the basic settings.
This procedure is necessary that you pay not twice for an already expanded feature.

## Slide 7: Identity code upgrade
If you are on the service page and click on the “Activation Key” button you run the “Activation Key” application.
Now type in your name
Your eMail address (it is only one address possible) if you need more you must define a rule in your email software.
Type in your internal reference number. This will help to find the right internal job.
Type in some internal notes. They will not be processed from somebody else automatically!
Then select the device type = D1Cb
Type in the 10 digit equipment number of the D1Cb
Match the identity code values which must be changed to your requirements.
Follow the requests and CONFIRM your input
Press <CREATE KEY>, tick ACCEPT, click OK
You will receive a email with the Activation Key data