## Slide 1: The new Sigma series (S1Cb, S2Cb, S3Cb)
Launchpackage S1Cb:
26. November 2012
Gabriele Hehl BPN
ProMinent Dosiertechnik GmbH - Heidelberg

## Slide 2: Sigma Control Series New
Sigma/ 3 – S3Cb
Sigma/ 2 – S2Cb
Sigma/ 1 – S1Cb
All Sigmas available

## Slide 3: ACHEMA 2012
Target for premium products:
Most possible innovation
Most possible flexibility
and at the same time
Possibility of customer-specific solutions

## Slide 4: Sigma /3 /2 /1 new – Technical features
Remote control unit as a standard e.g. Control unit can be entirely separated to protect the pump against unauthorized adjustment
Energy saving of thanks to Vector control 10 – 15 % at full load, 20 – 30 % at part load
Shutdown at overload / Torque (energy) monitoring
Realisation of variable dosing profiles

## Slide 5: Sigma/ 3/ 2 / 1 new – Energy monitoring
Torque (energy) monitoring
Energy saving by means of controlled motor magnetisation
Motor current
Magnetisation
Torque
Sigma current technology
Sigma new technology (Vector control)
Area of energy saving

## Slide 6: Sigma/ 3/ 2 / 1 new – Dosing profiles
Discharge stroke
Suction stroke
Discharge stroke
Suction stroke
Typical applications
Dosing of high viscous fluids
Reducing of NPSHr-value
Typical applications
Reducing pulsationing effects
Improving mixing when pump runs at lower speed

## Slide 7: Sigma/ 3 /2 /1 new - variety
Standard application (with HMI)
Project application (one for all-HMI)
Customer-specific solution (without HMI) (typical OEM-application)

## Slide 8: Conversion S_Ca -> S_Cb
Shutdown at overload for pump safety
No integrated pressure relief valve for Sigma Control type, …
…, but integrated bleed valve for manual de-aeration
. 0 . . . . . . . . . | without valve spring (standard)
. 1 . . . . . . . . . | with 2 valve springs, Hastelloy C, 0.1 bar
. 2 . . . . . . . . . | with bleed valve, seal FPM, without valve spring
. 3 . . . . . . . . . | with bleed valve, seal FPM, with valve spring
. 8 . . . . . . . . . | with bleed valve, seal EPDM, without valve spring
. 9 . . . . . . . . . | with bleed valve, seal EPDM, with valve spring

## Slide 9: Conversion S_Ca -> S_Cb
Fault indicating relay analogue to delta metering pump
          Freely programmable fault indicating relay:
          Relay-type: alarm, error, stopp, alarm+error, alarm+error+stopp
          Polarity: energised(NO) / deenergised (NC)
. . . . . . 0 . . . . | no relay
. . . . . . 1 . . . . | fault indicating relay (230V - 8A)
. . . . . . 3 . . . . | fault indicating relay + pacing relay (24V - 100mA)
. . . . . . 8 . . . . | 0/4-20 mA analogue output + fault indicating/pacing relay (24V - 100mA)

## Slide 10: Conversion S_Ca -> S_Cb
          Calibration as a standard
          Easy operation
          Freely programmable
          Modular concept – option modules delta / Sigma
          Operating lamps in HMI and pump foot
          Improved protection class IP65 / Temperature -10 ... +45 °C

## Slide 11: Sigma/ 3 /2 / 1 new – Sales start
          Sales start:
          Sigma/ 3 - August 2012
          Sigma/ 2 - September 2012
          Sigma/ 1 - November 2012
In order to ensure the availability of spare parts due to electronic parts of S_Ca phasing out, it won‘t be possible to order S3Ca, S2Ca and S1Ca from the following dates:
01.01.2013 – S3Ca
01.02.2013 – S2Ca
01.03.2013 – S1Ca

## Slide 12
Thank you for your attention!