## Slide 1
28 February 2018, Ulrich Markmann
CHLORINSITU® IIa

## Slide 2
Presentation Content
Description
Product Positioning
USPs
Functions
Specifications
Maintenance
Chlorinsitu® IIa

## Slide 3
Description new Chlorinsitu® IIa
The new Chlorinsitu® IIa combines well tried and robust technology with innovative compact design.
Except for the brine tank, all components could be integrated into one compact, space saving cabinet. The elaborate hydrogen discharge system allows an installation without additional requirements for a room ventilation (no ATEX requirements).
With the Plug & Play concept the system is ready for operation in no time and enables even untrained personnel to safely run the production.
The unit will automatically produce a sodium hypochlorite solution into the integrated storage tank. From this tank it can be drawn via the externally controlled chlorine pump and applied to the process.
The system will automatically start production and refill the product tank whenever it falls below a certain level.
The chlorate content of the product is well below the legal limits defined in EN 901.

## Slide 4
Chlorinsitu® IIa 60 g/h – 300 g/h
New range of open cell electrolysis
  Replaces Chlorinsitu® II
  Development started 06/2016
    Launch 03/2018
Unique selling points (USPs)
  Low investment electrolysis
  Plug & Play concept
  Simple controller with colour touch panel
  > 9 g/l FAC
  Low Salt Consumption ~3.0 kg/kg FAC
  Low Energy Consumption ~ 4.0 kWh/kg FAC
  Safe Integrated hydrogen discharge without ATEX requirements

## Slide 5
Type | Cell | Disinfectant | Capacity (g/h) | Main Applications
Chlorinsitu® II | Open-Cell | Hypochlorite (Bleach) 5 g/l | 400 – 2.400 | Low-end pools Potable water
Chlorinsitu® IIa | Open-Cell | Hypochlorite (Bleach) 9 g/l | 60 – 300 | Potable water Swimming pools
Chlorinsitu® III | Membrane | Hypochlorite (Bleach) 20-25 g/l | 50 – 10.000 | High-end pools Potable water Waste water Cooling water
Chlorinsitu® III Compact | Membrane | Hypochlorite (Bleach) 25 g/l | 25 and 50 | Small pools Potable water
Chlorinsitu® IV Compact | Membrane | Cl2 gas Caustic | 25 and 50 | Small pools Potable water
Chlorinsitu® V | Membrane | Cl2 gas Caustic | 25 – 3.700 | High-end pools Potable water Waste water
Chlorinsitu® V PLUS | Membrane | Cl2 gas Caustic Bleach 5-25 g/l (Plus) | 25 – 3.700 | High-end pools Potable water Waste water
DULCO®Lyse | Membrane | Hypochlorous acid 400ppm pH 6.5 | 100 - 300 | F&B industry CIP Inlet water treatment
Product positioning CHLORINSITU® IIa

## Slide 6
Unique Selling Points Chlorinsitu® IIa
Easy operation
  Fully automatic operation
  Only topping up of salt
  Colour touch HMI with clean menu structure
Cabinet Plug & Play concept
  Quick and easy installation; no extensive labour time and costs
  No ATEX problems
  No room ventilation required for safe operation
  Internal 50 litre chlorine product tank
  Internal chlorine dosing pump (optional)
  Level control for optional external chlorine product tank integrated
  Water softener integrated
State of the art quality chlorine
  High chlorine concentration FAC 9 g/l (old Chlorinsitu II – 5 g/l)
  Low chlorate, less than 4% of FAC
  Low chloride in product due to high salt efficiency

## Slide 7
USPs Chlorinsitu® IIa
Low consumptions
  Only 3,0 kg salt per kg chlorine
  Only 4,0 kWh/kg; high current efficiency (69%; 15% better than OSEC-L)
New and unique cell configuration
  Newly developed cell housing with optimized hydraulics
  Compact design with small footprint
  Benchmark yield and efficiency
Safety
  Hydrogen is separated from the product and actively evacuated
  No danger of hydrogen inside the plant room
  Less components and no pressurized parts leave less chance for leakage
  Automatic process control via sensors
  Drip pan with leakage detection
Remote access (optional)
  Remote Monitoring Software (remote engineer) for mobile devices and PC

## Slide 8
Components Chlorinsitu® IIa
Inlet Water Manometer
Inlet Water Filter
Primary Degassing Piping
Electrolysis Cells
Brine dilution with softened water
Inlet Temperature Sensor
Brine Pump
Solenoid Valve
(stops water flow during softener regeneration)
Softener
Leakage detection
Drip Pan
Plinth
Power Unit
Remote Engineer
Hydrogen Degassing Pipe
Product Pump (Chlorine Pump)
Micro Control Valve (Brine Dilution)
Product Tank

## Slide 9
Cabinet Chlorinsitu® IIa
Corrosion resistant Polyester reinforced fibreglass
Optional plinth to elevate total height to 1715 mm
Sealed IP54
Sizing:
  Height 1500 mm w/o plinth
  Width 750 mm
  Depth 620 mm

## Slide 10
New Electrolysis Cell
Innovative and unique cartridge design
Each cell produces 60 g chlorine/h
Installed in series to increase capacity
Very efficient flow path of the brine through cell results in outstanding efficiency:
  > 9 g/l chlorine @ only 3 kg salt / kg chlorine
High safety due to barrage that prevents dry-running of the electrodes
Long lifetime warranty 5 years @ 100% operation
Can be flushed with acid solution to be cleaned and restore capacity
Cell housing made from PVC-U

## Slide 11
Controller CIIa (HMI)
4.3“ Color display touch panel
USB Port
Ethernet interface
Easy to use / operate
Future standard in BU4-products
Exemplary: OZONFILT OZVb

## Slide 12
Flow Diagram Chlorinsitu® IIa
A = Inlet water
B = Softened water
C = Saturated brine
D = Diluted brine
E = Hydrogen
F = Product
G = Air
H = Diluted Hydrogen
1 = Optional product dosing pump
2 = Pressure gauge tap water
3 = Flow sensor cell output product
4 = Flow sensor cell input softened water
5 = Hypocell (1-5 depending on capacity)
6 = Tap water candle filter
7 = Drip pan
8 = Level sensor drip pan
9 = Air filter
10= Air flow sensor
11= Solenoid valve softened water (after softener)
12= Control valve dosing softened water (after flow sensor “4”)
13= Sample valve for testing softened water
14= Water softener
15= Brine dosing pump
16= Temperature sensor diluted brine cell input
17= Temperature sensor product cell output
18= Air fan
19= Level operated valve for filling brine tank
20= Salt tank

## Slide 13
Connections Chlorinsitu® IIa
Top view
A – Water supply
B – Brine supply
C – Brine supply softener
D – Filling brine tank
E – To external storage tank or process
F – Diluted hydrogen discharge
I – Power supply 230 VAC
J – Control signal internal product dosing pump (option)
K – Ethernet Cable (option)
N – Drip pan

## Slide 14
Installation Chlorinsitu® IIa
L – External product tank / Storage tank (optional)
M – Salt container
N – Chlorinsitu® IIa Cabinet

## Slide 15
Option: Chlorine Dosing Pump
Identcode option
Configuration fixed for each model/capacity of CIIa
When ordered without pump, customer can use own pump
Internal storage tank with 3 Level switches: too high, start/stop and empty (PLC inputs available)
Controlled externally via 0/4 - 20 mA or potential free contact
When an external product storage tank is used, the chlorine pump functions only as transfer pump and is controlled (on/off) by the CIIa
Chlorine Pumps:
60 g/h BT5B0713
120 g/h BT5B0420
180 g/h BT5B0232
240 g/h BT5B0232
300 g/h GMXA0245

## Slide 16
Softener (Option)
Integrated reliable softener
Protected by integrated pre-filtration of CIIa (50 micron, 10“ standard housing)
Preset to regenerate once every 48h
Electrical contact plus solenoid to prevent not-softened water to pass during regeneration

## Slide 17
Maintenance of CIIa
Maintenance Pack 1-yearly & 3-yearly
  Annual service kit for chlorine dosing pump
  Annual service kit for brine dosing pump
Cells can be flushed with acid solution once a year to remove eventual scaling and restore the initial efficiency
Cells are planned to be replaced (earliest) every 5 years
Yearly Maintenance includes (expected 2-4 h):
  Replacement of O-Rings and gaskets in contact with chlorine
  Exchange of water filter
  Exchange of air filter
  Cleaning of the salt tank if neccessary
  Acid flushing if neccessary
3-Yearly Maintenance also requires (4-6 h):
  Exchange of cell of flow sensor
  Cleaning of water softener
  5-Yearly Maintenance also requires:
  Exchange of cells
  Exchange water control micro valve
  Replace float switch of product tank
It´s electrolEasy!

## Slide 18
Acid flushing
Easy procedure to restore the initial capacity of the system in case it got decreased by scaling of the electrodes.
Recommended once a year during regular maintenance or when increasing voltage indicates scaling.
Procedure:
  Stop CIIa
  Flush cells with water (via HMI)
  Attach flushing pipe to the outlet of the cells and place end of pipe into a collection container
  Place brine suction hose into a container with HCl 5% and start brine pump. Pump HCl for 40 minutes.
  Flush cells with water again (via HMI)
  Remove flushing pipe and reconnect cell drain
  Re-Fill cells with brine (via HMI)
  Start operation

## Slide 19
Salt specifications for CIIa (based on DIN EN 973:2009-12, extended)
NaCl-Content of dried product | > [%] | 99,4
Anticaking Hexacyanoferate [Fe(CN6)]4- | max. mg/kg | 20
Water-insoluble substances | max. [%] of NaCl content | 0,05
Moisture content of dried product | max. [%] of NaCl content | 0,6
Moisture content of undried product | max. [%] of NaCl content | 5
Calcium + Magnesium (Ca + Mg) | max. [mg/kg] | 100
Arsenic (As) | max. [mg/kg] | 13
Cadmium (Cd) | max. [mg/kg] | 1,3
Chromium (Cr) | max. [mg/kg] | 13
Mercury (Hg) | max. [mg/kg] | 0,26
Nickel (Ni) | max. [mg/kg] | 13
Lead (Pb) | max. [mg/kg] | 13
Antimony (Sb) | max. [mg/kg] | 2,6
Selenium (Se) | max. [mg/kg] | 2,6
Manganese (Mn) | max. [mg/kg] | 10
Iron (Fe) | max. [mg/kg] | 10

## Slide 20
Features
Remote Control Engineer
  Improved accessibility of installations
  Possibility of assistance long distance
  No firewall problems
No ATEX-rating
  Hydrogen degassing is regarded with active ventilation of the cabinet and the product tank
Very low Chlorate
  DIN EN 90116: 5.4% Chlorate based on FAC in sodium hypochlorite solution for disinfection of drinking water
  CIIa: < 4% Chlorate

## Slide 21
Simple operation
Low chlorate product
Robust design
Simplified technology
High efficiency
Space saving
Low maintenance
No ATEX requirements
FAC concentration 9 g/h
3 kg salt per kg FAC
CHLORINSITU® IIa (60 g/h – 300 g/h)

## Slide 22
Any questions ?
Thank you for your attention