## Slide 1: Chlorine Dioxide
ProMinent Fluid Controls, Inc.

## Slide 2: ProMinent ClO2 System
Pre-cursor chemicals:
    Sodium Chlorite (7.5% & 25%)
    Hydrochloric Acid (9% and 33%)
    Metering pump accuracy (no venturi)
Generates a 2% (20,000 ppm solution)
    80-90% Yield
    Chlorine-free solution (no hypo or gas)
    No THM’s or pH concerns
    No chloramine formation

## Slide 3: ProMinent BelloZon CDVc

## Slide 4: Bello Zon CDVc for Diluted Chemicals
PVDF reactor and reactor-outlet
reactor cover for protection
purge assembly for reactor (optional)
static mixer
Backpanel for wall mounting
metering pumps in CAN-bus version
controller with data logger and screen recorder
calibration and suction aid with vacuum pump (optional)
single stroke flow sensor

## Slide 5: Capacity Range CDVc (dilute chemicals)
Model | ClO2 output [g/h] | operating pressure [psi] | operating temperature [°C]
CDVc 20 | 1-20 | 116 | 10-40
CDVc 45 | 2-45 | 116 | 10-40
CDVc 120 | 6-120 | 116 | 10-40
CDVc 240 | 12-240 | 102 | 10-40
CDVc 600 | 30-600 | 73 | 15-40
CDVc 2000 | 100-2,000 | 29 | 15-40

## Slide 6: CDVc Changes
Retired:
  CDVb 15, 35, 60, 220, 400 models
Pressure changes:
  CDVc 600 (derated) 116 psi –> 73 psi
  CDVc 2000 (derated) 102 psi –> 29 psi

## Slide 7: New CDVc Features
Data logging (+400 days)
Communication interfaces
Direct measurement of ClO2 and chlorite
PVDF Reactor
Larger physical size

## Slide 8: Capacity Range CDKc (concentrated chemicals)
Model | ClO2 output [g/h] | operating pressure [psi] | operating temperature [°C]
CDKc 170 | 170 | 116 | 10-40
CDKc 420 | 420 | 116 | 10-40
CDKc 900 | 900 | 116 | 10-40
CDKc 2100 | 2,100 | 102 | 10-40
CDKc 3000 | 3,000 | 73 | 15-40
CDKc 7500 | 7,500 | 29 | 15-40

## Slide 9: CDKc Changes
Retired:
  CDKc 150, 750, 1500, 6000, 10,000 models
Pressure changes:
  None

## Slide 10: Series CDVc and CDKc
Direct connection of 2 amperometric sensors: measurement/display of ClO2 and chlorite
Multiple Interfaces
  Profibus DP
  LAN
  WEB-server
  ISDN (dig/net)
  Analog
  GSM (glob/mob)

## Slide 11: Chlorine Dioxide and Chlorite Analysis
D1C: ClO2, chlorite, pH, ORP
  Single variable
D2C: ClO2 + pH
  Dual variable
Photometer: DT4 ClO2 + chlorite

## Slide 12: Probes for Chlorine Dioxide and Chlorite
Dulcotest CDE 2 for chlorine dioxide
  3 measuring ranges (10, 2, and 0.5 ppm)
Dulcotest CDP 1 (2 ppm) for chlorine dioxide
  special probe for process water contaminated with detergents (bottle washing machine, CIP-plants)
Dulcotest CLT 1 for chlorite
  2 measuring ranges (2 and 0.5 ppm)

## Slide 13: Safety Features
Generated solution is only 2% (20,000 ppm)
Operate well below max conditions
>8,000 ppm (300 g/m3) is explosive
We operate at 1,000 ppm
Isolated in an enclosed reactor housing
Reactor housing is automatically purged via an injector and solenoid valve up to 6 times per hour (every 10 minutes)
The reactor chamber is always full of solution – not gas

## Slide 14: Safety Features
Flow sensor on bypass water line adjusts the amount of chlorine dioxide generated
Chlorine dioxide injection into the bypass water flow
Output is controlled by a ProMinent chlorine dioxide residual controller
Metering pump flow sensor
Wall mounted ClO2 gas monitor (option)

## Slide 15: System Maintenance
ProMinent personnel can do start-up (fee)
Advise Pittsburgh training
ProMinent yearly service contract available
    Rebuild and calibration of pumps
    Inspect reactor and piping
    System check
Spare parts kits available for each model

## Slide 16: Chlorite and Acid Suppliers
  Vulcan
  Harcross Chemical
  Global Technologies
  DuPont Water Technologies
  Sigma-Aldrich